## Slide 1
Module 3: Transportation and Transfer of Ethanol-Blended Fuels

## Slide 2: Objective
<number>
Upon the successful completion of this module, participants will be able to describe how ethanol-blended fuels are transported and transferred and where the most likely points for error in these actions will exist.

## Slide 3: Introduction
<number>
Essential to quickly & effectively identify presence of ethanol / ethanol-blended fuels at scene of incident
Can be challenging because containers in which ethanol is transported not always clearly marked
Steps taken to ensure incidents managed effectively

## Slide 4: Transportation and Placarding
<number>
Gasoline & ethanol-blended fuels transported in same general types of containers & tanks
MC-306 / DOT-406
Copyright 2006, TEEX/ESTI

## Slide 5: Transportation and Placarding
<number>
DOT:
  Classifies according to primary danger
  Assigns standardized symbols to identify classes
Ethanol & ethanol-fuel blends in flammable liquids
Copyright ERG
Notes: Reprinted from the DOT Emergency Response Guidebook, http://hazmat.dot.gov/pubs/erg/gydebook.htm

## Slide 6: Transportation and Placarding
<number>
Tanker placards:
  Lower ethanol concentrations up to & including E-10 blended fuels: UN 1203 flammable placard
  E-85: UN 3475 flammable placard
  E-95: UN / NA 1987 flammable placard
Copyright ERG
Notes: Reprinted from the DOT Emergency Response Guidebook, http://hazmat.dot.gov/pubs/erg/gydebook.htm

## Slide 7: Transportation and Placarding
<number>
Rail tanks identified similarly
Pressure & vacuum relief devices same as currently found on gasoline-style transport tankers
Bottom loaded & unloaded by standard 4-inch quick connect / direct connections

## Slide 8: Transportation and Placarding
<number>
Valving internal to tanks with breakaway piping & remote shut-off controls
Vapor recovery systems same as currently found on gasoline tankers

## Slide 9: Transportation and Placarding
<number>
Most E-95 transported by rail:
  Some by waterway & very small amounts by pipeline
Storage depots with no access to rail receive it by road tankers:
  Trans-loading

## Slide 10: Transportation and Placarding
<number>
NFPA 704 diamond:
  Uses colors, numbers, & special symbols to indicate presence of hazardous materials
  Higher number = greater hazard

## Slide 11: NFPA 704 Diamond
<number>
Copyright 2008, TEEX/ESTI

## Slide 12: Transportation and Placarding
<number>
NFPA 704 diamond:
  Health: Blue
  Flammability: Red
  Reactivity: Yellow
  Special: White (special notice)

## Slide 13: Transportation and Placarding
<number>
NFPA diamond for E-100, E-95, E-85, & gasoline:
  1: Blue health square: slight to moderate irritation
  0: Reactivity yellow square
  3: Flammability red square: high flammability with ignition likely under most conditions
  No commonly accepted special character (white)

## Slide 14: NFPA Diamond for E-100, E-95, E-85, and Gasoline
<number>
Copyright 2008, TEEX/ESTI

## Slide 15: Transportation and Placarding
<number>
Most hazardous materials incidents occur during transportation & transfer operations
Be aware of areas / routes where large shipments of ethanol & ethanol-blended fuels routinely pass
E-95 now leading single hazardous material transported by rail

## Slide 16: Transportation and Placarding
<number>
Most of Midwest & other ethanol production facilities have access to rail sidings, many bulk storage fuel depots do not have rail sidings:
  Much of E-95 off-loaded & transferred to tanker trucks for distribution to bulk storage facilities via highways

## Slide 17: Transportation and Placarding
<number>
Placards able to indicate high-concentration ethanol-blended fuels:
  Does not distinguish between gasoline & E-10 gasohol
  E-10 requires AR foam for emergency response
TRANSCAER

## Slide 18: Activity 3.1 — Ethanol Spill Emergency
<number>
Purpose:
  To allow participants to determine the hazards associated with an ethanol emergency.

## Slide 19: Summary
<number>
Variety of sources for information about chemicals involved in spill / fire incidents:
  MSDS
  UN numbers
  DOT placards
  NFPA 704 placards
E-95 become leading hazardous material transported by rail:
  Transfer commonly occurs via highways