## Slide 1
Module 4: Storage and Dispensing Locations

## Slide 2: Objective
<number>
Upon the successful completion of this module, participants will be able to discuss common and unusual needs for storage and dispensing of ethanol-blended fuels.

## Slide 3: Introduction
<number>
Often fail to think of gas stations when thinking of ethanol-blended fuels
Believe if there is no bulk storage operation / production operation in jurisdiction, have little to worry about

## Slide 4: Terminal Storage of Ethanol-Blended Fuels
<number>
Denatured E-95 most common ethanol blend in storage in terminals & tank farms
Other formulations blended during loading process for transport:
  Bottom-loading 2 components into tanker trucks
  Go through in-line mixing / static mixing systems prior to bottom loading process

## Slide 5: Terminal Storage of Ethanol-Blended Fuels
<number>
E-95 typically stored in conventional carbon steel storage tanks:
  May be smaller than other tanks at terminal
3 general types of storage tanks:
  Cone roof (closed-top) tanks
  External floating roof (EFR) tanks have open top with a floating pan
  Internal floating roof (IFR) tanks with closed top & internal floating pan

## Slide 6: Terminal Storage of Ethanol-Blended Fuels
<number>
Commonly delivered via tank truck / rail car / barge:
  Currently no common pipeline delivery method
E-95 normally stored in IFR tanks
Copyright 2006, TEEX/ESTI

## Slide 7: Terminal Storage of Ethanol-Blended Fuels
<number>
Built-in fire protection systems:
  Fixed systems:
    Combination of devices permanently installed
    Provide fire protection
    Can be activated manually / by detection device

## Slide 8: Terminal Storage of Ethanol-Blended Fuels
<number>
Built-in fire protection systems:
  Systems may no longer be appropriate
  Rendered inoperable at onset / during fire or explosion emergency

## Slide 9: Terminal Storage of Ethanol-Blended Fuels
<number>
Preplanning for potential events at tank farm facilities extremely important
Fire departments that help provide protection to tank farm facilities should have:
  Access to high-flow fire fighting foam equipment
  Large supplies of compatible foam available on hand

## Slide 10: Terminal Storage of Ethanol-Blended Fuels
<number>
Consortiums between multiple tank farm operations & fire department
Built-in fire suppression systems currently best protection for large storage tanks
Fire department personnel should be familiar with systems & pre-calculate required flow rates
Preplan operations supplying systems
Practice exercise at least annually

## Slide 11: Terminal Storage of Ethanol-Blended Fuels
<number>
Challenges:
  Provide limited access for fire fighting equipment
  May be inadequate water supplies in area
  Personnel may have to contend with containment dikes & their systems
  May be miles of exposed product piping involved
  May be unprotected loading rack facilities

## Slide 12: Terminal Storage of Ethanol-Blended Fuels
<number>
Pre-fire planning extremely important
Pre-established working relations between fire department & facility operators

## Slide 13: Bulk Plant and Distribution Facilities
<number>
Smaller bulk distribution storage facilities may pose greatest challenge to local fire departments
Flammable liquid fuels stored at facilities in modest quantities

## Slide 14: Bulk Plant and Distribution Facilities
<number>
Gasoline / Ethanol-blended fuel normally stored in underground tanks / small volume above-ground steel tanks
Vertical / Horizontal design
Most likely E-10 mixture
Most do not have built-in fire protection systems

## Slide 15: Bulk Plant and Distribution Facilities
<number>
Spill diking usually designed to contain largest tank in facility
Incidents involving multiple tanks in facility may overtax designed containment area

## Slide 16: Retail Dispensing Stations
<number>
Majority have underground storage tanks
Relatively small in storage volume, large in number throughout country
May / May not have vapor recovery systems associated with sites
Larger volume gas stations may have above-ground storage tanks

## Slide 17: Retail Dispensing Stations
<number>
Filled by tankers
Early 2008: over 1,000 fueling sites handling E-85
Thousands more handling E-10
Number expected to increase

## Slide 18: Retail Dispensing Stations
<number>
Stored in horizontal underground tanks:
  Maximum pressure 0.5 psig
  Tank capacities
  Typically constructed of steel & double walled
Property of Hildebrand and Noll, reprinted with permission
Notes: Reprinted with permission from Storage Tank Emergencies, Copyright 1997 by Michael Hildebrand & Gregory G. Noll

## Slide 19: Retail Dispensing Stations
<number>
Stored in horizontal underground tanks:
  Emergency shut-off valves vary
  Loading & unloading points vary
  Risers for multiple tanks color-coded / marked to identify product

## Slide 20: Summary
<number>
Most commonly found ethanol-blended fuel at terminal facilities is E-95
Fixed fire suppression systems often rendered inoperable at onset of incident
Preplanning for potential events at tank farm facilities extremely important:
  Sources of mutual aid
Amount of fuel stored at each station small, sheer number may be cause for concern

## Slide 21: Activity 4.1 — Ethanol in Your Jurisdiction
<number>
Purpose:
  To allow participants to determine the potential for ethanol emergency in their jurisdictions.