## Slide 1
Module II:
Basic Electrical
Concepts
And Hazards

## Slide 2
Describe basic electrical concepts that pertain to P/HEVs and EVs.
Terminal Objective
Define basic electrical terms.
Compare and contrast AC and DC electricity.
Identify how electricity affects the body.
Enabling Objectives
Module II Objectives

## Slide 3
Voltage
Electrical potential. Comparable to water pressure
or pounds per square inch (PSI) in a hose.
Measured in Volts
Current
Quantity of electrons flowing. Comparable
to gallons per minute (GPM) flow of a hose.
Measured in Amperes
Definitions
Resistance
Material’s resistance to conducting current.
Comparable to friction loss in a hose line.
Measured in Ohms

## Slide 4
Alternating Current
Current repeatedly reverses direction.
Hybrid Electric Vehicle
Direct Current Vs. Alternating Current
Direct Current
Current always flows in the same direction.

## Slide 5
Hybrid Electric Vehicle
DC Circuits
Typically found in electronic devices that utilize battery power and some industrial applications.
AC Circuits
Found anywhere electricity is supplied by the utility company from the power grid, such as in buildings.

## Slide 6
With both AC and DC, there must
be a completed path, or circuit, for
current to flow.
A switch creates a break in the
circuit when “OFF”.
Turning the switch “ON” completes
the circuit, allowing current to flow.
Injury can occur when a person’s
body becomes part of a circuit by
completing a path for current.
Understanding Electrical Circuits
OFF
ON

## Slide 7
DC power sources have
a positive and a
negative terminal.
Current flows from
negative side of
battery, through the
circuit, to positive
side of battery.
DC Circuits

## Slide 8
Contacting one side will not result in shock because circuit is not completed.
Contacting both sides will complete the circuit and can result in shock.
DC Circuits

## Slide 9
Instead, of positive and
negative, AC circuits have
“hot” and neutral
conductors.
In some wiring
configurations, the
neutral can carry current.
A grounding conductor
allows current to flow
into the earth in the
event of a hazard or fault.
AC Circuits

## Slide 10
Unlike DC circuits,
most AC circuits can
be dangerous when
touching only one
hot conductor if you
are grounded.
AC Circuits
Current can flow
through you into
the earth to
complete a circuit.

## Slide 11
High Voltage Circuits in Vehicles
HV
POWER
SOURCE
ELECTRIC
MOTOR
Some P/HEVs and EVs use AC powered motors
requiring AC circuits as well.
High Voltage circuits in
vehicles are isolated,
and are not grounded
to the chassis or
the earth.
Current does not
seek earth ground
like in a building.
All P/HEVs and EVs use DC high voltage systems.

## Slide 12
If the chassis becomes
part of an HV circuit,
the system is designed
to detect the fault
and shut down.
High Voltage Circuits in Vehicles
HV
POWER
SOURCE
ELECTRIC
MOTOR
Since it is not seeking earth ground, to get a
shock, you must contact two points in the circuit.
Contacting only one should not create a circuit to
ground as it would in a building.
Current will not
follow a hose stream.

## Slide 13
Human body and PPE provide some
resistance to electricity.
How Electricity Affects the Body
Voltage must be high
enough to overcome
resistance before it
can enter your body.
Environmental
conditions, like
being wet, can
greatly reduce
resistance.

## Slide 14
How Electricity Affects the Body
Once resistance is
overcome, Amperage
usually determines
degree of damage.
Circuits in P/HEVs and
EVs have both the
voltage and amperage
to be considered
highly dangerous.

## Slide 15
OBSERVABLE EFFECT
240
70
40
Startle Reaction
Can’t let go
Electrical Burns
Possible Ventricular Fibrillation
Milliamps (1000 mA = 1 A)
2
DC Current Effect on Humans
Some models of P/HEV and EV generate current in excess of 100 Amps, or 100,000 mA
1
2
Effect thresholds based on full grown adult physiology. Effects on smaller persons or children may occur at lower amperage.
Personnel Protection Devices for Specific Applications, Electric Power Research Institute, Project 6850-02, Final Report, October 1999, prepared by Underwriters Laboratories Inc.
1
2

## Slide 16
AC Current Effect on Humans
OBSERVABLE EFFECT
833
105
70
20
6
6
.5
Startle Reaction
GFCI will trip
Can’t let go
Muscle Contraction (Respiratory Paralysis)
Electrical Burns
Ventricular Fibrillation
Current Used by a 100 Watt Light Bulb
Milliamps (1000 mA = 1 A)
Effect thresholds based on full grown adult physiology. Effects on smaller persons or children may occur at lower amperage.
Personnel Protection Devices for Specific Applications, Electric Power Research Institute, Project 6850-02, Final Report, October 1999, prepared by Underwriters Laboratories Inc.
1
1
2
2
Some models of P/HEV and EV generate current in excess of 100 Amps, or 100,000 mA
Notes: Added mA/Amp

## Slide 17
?
1.
What is the difference between Voltage and Current?

## Slide 18
Voltage is the electrical potential of a circuit, or the “pressure” of the current.
Current is the rate of flow, measured in amperes or amps.
Answer

## Slide 19
?
2.
In which electrical system is the current always flowing in the same direction?

## Slide 20
Direct Current
DC
Answer

## Slide 21
?
3.
Which of the following statements about the hazards of DC electricity is correct?
A.
B.
To be harmed by DC current, contact with both the positive and negative side must be made.
To be harmed by DC current, contact must be made with only one side.

## Slide 22
A. To be harmed by DC current, contact with both the positive and negative side must be made.
Answer

## Slide 23
?
4.
Will electricity from the vehicle’s AC high voltage system travel through the water in a hose stream back to the responder?

## Slide 24
No, because the AC system in vehicles does not seek ground.
Answer

## Slide 25
?
5.
Does being wet increase or decrease the skin’s resistance to electricity?

## Slide 26
Wetting the skin decreases the resistance to electricity and intensifies the impact of the current on the body.
Answer

## Slide 27
Definition of Voltage, Current,
and Resistance.
Direct Current vs. Alternating Current.
How Electricity Flows.
How Electricity Affects the Body.
Module Summary